Block schematic
Low jitter time distribution system,
Y. Acremann, 2.2.2021

---
Transmitter
M-RAM
MR25H128
SPI
For precision receivers
SPI
AD9543
(jitter cleaner,
clk distribution)
FPGA
(MAX 10)
Logic,
CPU
Serializer
SCAN-
921025H
Fan-out
buffer
NB3L8504S
driver
DS15BA101
RJ-45
cable
Pulse-ID
8b/10b
80 MHz
driver
DS15BA101
RJ-45
cable
100 Hz
driver
DS15BA101
RJ-45
cable
UART,
JTAG
(CPU)
driver
DS15BA101
RJ-45
cable
LVDS to LVCMOS
SN65LVDS4
USB – Serial
FT2232
(for debugging)
USB
800 Mbit/s signals with embedded clock
Config data
80 MHz clk
Pulse-ID
100 Hz

---
Concept
- Bit clock synchronized to the oscillator (80 MHz) for precision timing (estimate: 10 ps jitter)
- Jitter cleaner to get very clean clock signals from 80 MHz clock
- FPGA:
- Counting of 100 Hz pulses (pulse-ID)
- Control of the serializer and M-RAM
- CPU for configuration of the jitter cleaner
- M-RAM: Stores the last pulse-ID (restore after power-loss)
- Distribution: RJ-45 cabes, max. length: 70m
- Encoding:
- For simple receivers: 10 Mbit/s 8b/10b encoded data => jitter: 100 ns
- For precision receivers: 800 Mbit/s 8b/10b encoded data (+ start bit)

---
Receiver
USB – Serial
FT2232
(for debugging)
USB
Input
FPGA
(MAX 10)
Logic,
CPU
RJ-45
cable
receiver (2x)
DS15EA101
De-Serializer
SCAN-
921226H
Pulse-id
Trigger
Lock
Time stamp
(to frame grabber)
AD9543
(jitter cleaner,
clk distribution)
SPI
RJ-45
cable
driver (2x)
DS15BA101
Low-jitter
trigger
Output to another receiver
LVDS to LVCMOS
SN65LVDS4
Config data (not time critical)
80 MHz clk
Pulse-id
100 Hz

---
Additional features: Receiver
- Power over the RJ-45 cable to the receivers
- Trigger outputs:
- Several independent outputs
- Low jitter
- Time steps in 1/(80 MHz)
- Output connector to connect another receiver